## Slide 1: Humanoid Robot Control using Orbital Energy of the Variable Height Inverted Pendulum
Prof. G. Oriolo
Prof. L. Lanari
Supervisor: N. Scianca
Underactuated Robots, A.Y. 2020/2021
Leonardo Salustri (M1762556)
Paolo Sebeto (M1894763)
Francesco Scotti (M1758391)

## Slide 2: Introduction
LIP is the simplest model for bipedal walking:
All the mass of the robot is considered to be concentrated at its Center of Mass (CoM) with massless telescopic leg.
It’s not possible generate CoM height variations, as the hypothesis of constant CoM height is required to keep the model linear.
1
How to plan a gait introducing a variable CoM height trajectory ?
Variable height Inverted Pendulum, with Orbital Energy Control

## Slide 3: Orbital Energy
It is a conservative quantity.
Can be seen as the sum of the kinetic energy and the potential one of a mass spring system with a negative elastic term.
LIP is a restricting model, since it requires a constant height.
A conserved orbital energy exists for any height trajectory .
The idea is to generate a trajectory for the CoM through the energy level of the system and consider a variable height profile for the CoM.
2

## Slide 4: Variable Height Inverted Pendulum
Consider a 2D motion in the xz-plane.
It is assumed that the ZMP is on the foot contact point, always at the origin of the reference frame.
We want the ground reaction force to be able to mantain the virtual holonomic constraint z = f(x).
This constraint is treated as a manifold in the system’s 4-dimensional state space defined by: σ = z – f(x) = 0
3
with q = [x z]T

## Slide 5: Variable Height Inverted Pendulum
Parametrizing the ground reaction force as fgr = mqu where:
The unconstrained d.o.f. x and the complete dynamics are respectively:
This single control input (u ≧ 0) is used to control both horizontal and vertical CoM position.
4
with q = [x z]T

## Slide 6: Conditions for Balance
With balance, we refer to asymptotic convergence to a fixed point of the dynamics at a specified desired final height zf > 0.
Reaching balance practically means to stop the walking motion of the robot within a step, at a desired CoM height.
Starting from any state x =() convergence to a fixed point requires satisfying the condition
5

## Slide 7
6

## Slide 8: Derivation of height trajectory
First of all, given an initial state x0 = we enforce the two initial conditions: and
The balance conditions requires, for the Orbital energy associated to f, to satisfy:
7
with:

## Slide 9: Cubic Polynomial f(x)
8
Restricting the class of trajectories to polynomials, the integral in Edes is computable in closed form as:
Final desired height

## Slide 10: The Controller u
The general expression for the control u is:
Given f(x) as polynomial function and x, we can derive u in closed form as a rational function of x and x0.
9
with:

## Slide 11: Step Simulation with the Controller u
10

## Slide 12: Clipped Variant Control
The orbital energy controller u can not pull on the ground.
11

## Slide 13: Region of attraction
Unilateral control u ≧ 0.
Considering a first-order formula, i.e. an expression written combining a set of polynomial equations and inequalities (in variables y1,…yn) using the logical conjuction (⋀), disjuction (⋁), and negation (¬) operators, we obtained:
12

## Slide 14
Region of attraction
13

## Slide 15: Velocity Control
Let vdes be the desired velocity at the top of the next stride (when x = 0), then:
Equating these two expressions, and solving for x0, we get the location to step in order to achieve the desired vdes
It is important to have a smooth connection between consecutive functions f(x) at each step, so:
14

## Slide 16: Simulation settings
The support leg is actuated to control the body’s height as a function of the horizontal distance from the foot to the body mass.
PD control plus a feed-forward computed torque command:
We have used a symmetric polynomial f(x) = a0 + a2x2 + a4x4 , with f(x) = z* if |x| ≧ x* with x* = corresponding to the point of zero slope of the polynomial. (a0 = 0.9375, a2 = -2, a4 = 30.864)
15

## Slide 17: Multiple choices for x0
16
Since the previous equation relative to Edes has multiple solutions w.r.t. x0 if we choose a step sufficiently large considering a starting , the robot can’t do it. So it falls down!

## Slide 18: Simulation with variable vdes
17

## Slide 19: Simulation with variable vdes
18

## Slide 20: Simulation with variable vdes
19

## Slide 21: Simulation with variable step size
20

## Slide 22: Simulation with variable step size
21

## Slide 23: Simulation with variable step size
22

## Slide 24: MPC for variable CoM height
The key idea is to control the robot through the definition of two relevant trajectories.
The goal is to develop a trajectory for the zmp which guarantees a balance condition.
It is imposed a virtual vertical dynamic such that the resultant dynamic is a 3D LIP.
23

## Slide 25: MPC for variable CoM height
ZMP constraints:
Stability constraints considering
anticipative tails:
24

## Slide 26: Simulation results
25

## Slide 27: Simulation results
26

## Slide 28: Conclusions
27
MPC
Orbital energy
Computationally more intensive
Stability issues tackled directly
Lack of prediction
Limitation of the point-foot assumption
Possibility of imposing directly the CoM trajectory

## Slide 29
Thank you for the attention!
Leonardo Salustri (M1762556)
Paolo Sebeto (M1894763)
Francesco Scotti (M1758391)